## Slide 1: VNL v.2.1 Readme
1. There was a bug in the v2 annual averaging that has been resolved. The annual average radiance is calculated as a weighted average using the formula: (Sum of the monthly average radiances times the number of cloud-free coverages from that month)/the total number of cloud-free coverages in the year. In some cases, the monthly average radiances were being paired with a different month's cloud-free coverages. This has been corrected.
2. In VNL v2 radiance thresholds are applied to filter out (returned to the multiyear background) grid cells detected only one or two times from the full set of years. The average radiance threshold for grid cells detected once is 0.7 nanowatt and the threshold for gird cells detected twice is 0.5 nanowatts. This filtering has been removed in VNL v2.1.

## Slide 2: VNL v.2.2 Readme
In VNL v 2.2 VIIRS data from multiple satellites have been used. It is a combination of 11 months’ data from SNPP, excluding 202208. Because of glitches in the SNPP satellite there are no data for the first 10 days of August, so SNPP 202208 was excluded. Instead, data from 3 months of NOAA-20 – 202205, 202208 and 202209 were added to make the annual composite.
In VNL v2, and v2.1, the median calculation excludes months with less than 3 cloud-free coverages. The v2.2, however, includes any month with more than one cloud-free coverage.
In calculating the data range, for VNL v2, grid cells having zero cloud-free coverages and having median placeholder values of -1.5 were included. In v2.1, grid cells having zero cloud-free coverages, and marked with median values of zero were included. In v2.2, all grid cells lacking median values were excluded.

## Slide 3
Monthly DNB Composites
Average Radiance
Cloud-free observations
Total observations
Aurora Filtering
Raise DR threshold to 1.0 in north aurora zone. Zero out radiances in south aurora zone.
Multiyear DNB Composites
Max of median radiances
3x3 Max median data range
Percent cloud-free observations
Multiyear DR Threshold Grid
From % cloud-free versus DR scattergram for confirmed background areas.
Multiyear Masked Median
Draw north and south auroral zone vector polygons
Annual DR Masked Medians
Zero out radiances in grid cells where DR is below threshold.
Multiyear Detection Tally
Define mask for detection tallies of 1 and 2 across annual time series.
North Aurora Cleanup
Apply residual aurora off mask to zero out aurora noise in masked medians.
Annual DNB Composites
Skip months with less than 3 cloud-free observations
Total observations
Cloud-free observations
Min, max, average, and median radiance grids
3x3 data range from median
Multiyear Masked Median
Draw vector polygons on residual aurora features for masking.
Low Tally Cleanup
Apply tally 1 and 2 off mask with masked median radiance threshold of 0.7 nW/cm2/sr for single detections and 0.5 for double detections.
Annual Masked Radiances
Apply lit grid cell mask to the annual average and median radiance grids.
VNL V.2

## Slide 4
Monthly DNB Composites
Average Radiance
Cloud-free observations
Total observations
Aurora Filtering
Raise DR threshold to 1.0 in north aurora zone. Zero out radiances in south aurora zone.
Multiyear DNB Composites
Max of median radiances
3x3 Max median data range
Percent cloud-free observations
Multiyear DR Threshold Grid
From % cloud-free versus DR scattergram for confirmed background areas.
Multiyear Masked Median
Draw north and south auroral zone vector polygons
Annual DR Masked Medians
Zero out radiances in grid cells where DR is below threshold.
North Aurora Cleanup
Apply residual aurora off mask to zero out aurora noise in masked medians.
Annual DNB Composites
Skip months with less than 3 cloud-free observations
Total observations
Cloud-free observations
Min, max, average, and median radiance grids
3x3 data range from median
Multiyear Masked Median
Draw vector polygons on residual aurora features for masking.
Annual Masked Radiances
Apply lit grid cell mask to the annual average and median radiance grids.
VNL V.2.1

## Slide 5
Monthly DNB Composites
Average Radiance
Cloud-free observations
Total observations
Aurora Filtering
Raise DR threshold to 1.0 in north aurora zone. Zero out radiances in south aurora zone.
Multiyear DNB Composites
Max of median radiances
3x3 Max median data range
Percent cloud-free observations
Multiyear DR Threshold Grid
From % cloud-free versus DR scattergram for confirmed background areas.
Multiyear Masked Median
Draw north and south auroral zone vector polygons
Annual DR Masked Medians
Zero out radiances in grid cells where DR is below threshold.
North Aurora Cleanup
Apply residual aurora off mask to zero out aurora noise in masked medians.
Annual DNB Composites
Mix of VIIRS data from multiple satellites
Skip months with less than 1 cloud-free observations
Total observations
Cloud-free observations
Min, max, average, and median radiance grids
3x3 data range from median
Multiyear Masked Median
Draw vector polygons on residual aurora features for masking.
Annual Masked Radiances
Apply lit grid cell mask to the annual average and median radiance grids.
VNL V.2.2